## Slide 1: D200F Applications, Programs and Indentures
August 2021

## Slide 2
D200F Applications, Programs
and Indentures
Welcome
Online Delivery
Daily Schedule
Breaks
Assignments
Quiz

## Slide 3
Module 1 – Introduction to API
Module 2 – Terms and Definitions
Module 3 – Applications, Programs, and Indentures
Module 4 – API Subsystem
3
Introduces RMS and API systems
Configuration management
Interchangeability and Substitutability
Secondary items, ERRC codes, and NSNs
Applications, Programs, and Indentures
Illustrated Parts Breakdown (IPB)
API subsystem
Data elements, indenture formulas, and file maintenance
Course Overview

## Slide 4: Module 1 - Introduction to API
4
NOTE: D200F API is the database that houses our indenture structures and application records used in requirements computations.
SPM is used to handle requirements computations. For the foreseeable future, API will be maintained and will supply data to SPM via ODS.
Introduction to API

## Slide 5: Module 1 - Introduction to API
5
Lesson 1a
D200 Requirements Management System (RMS)
Introduction to API

## Slide 6
6
Lesson Preview
Explains who has responsibility for determining materiel requirements
Describes goal of AFMC when determining requirements
Explains purpose of requirements computations
Describes D200 RMS system and some subsystems, including API
Introduction to API

## Slide 7: Module 1 - Introduction to API
7
AFMC determines materiel requirements for AF assets
Requirement computation = identifying materiel needs and securing necessary assets
Goal of AFMC is to provide maximum supply support at minimum taxpayer cost
Reporting of usage, assets, and special conditions affecting requirements computations
Introduction to API

## Slide 8: Module 1 - Introduction to API
8
Requirements computations help meet the diverse needs of the Air Force
Introduction to API

## Slide 9: Module 1 - Introduction to API
Correct computations = successful budget defense
9
Funding
All AF programs depend on funds from Congress
BES (Budget Estimate Submission) is an end product of requirements computations
Introduction to API

## Slide 10: Module 1 - Introduction to API
10
SPM
Manages all information used in the computation of requirements
A software systems that processes item demand and usage
Stores data within SPM
Introduction to API

## Slide 11: Module 1 - Introduction to API
11
RMS
Incorporates many subsystems:
  D200C/EIP, D200E/RIID, D200F/API, D200H/IRD, D200N/CSIS
Introduction to API
Notes: D200C/EIP – Equipment Item process -
D200E/RIID – Requirements item identification Data – (provides cataloging data and stock list changes received from the Master Item identification control system (D043))
D200F/API – Applications, programs, indentures – (approved system of record for API data; It establishes a secondary item application or configuration file for each weapon system to support readiness-based sparing computations.)
D200H/IRD – Initial Requirements Determination – (subsystem is the preferred input source for program checklist)
D200N/CSIS – Central Secondary item Stratification – (display budget and repair deficits for each requirements segment by fiscal year; provides data on asset distribution against requirements and is used as a baseline for inventory analysis)

## Slide 12: Module 1 - Introduction to API
12
API
Foundation for RMS
Accuracy of RMS computations attributable to accuracy of API
Supplies parts list, application data, program data for requirements computations
Introduction to API

## Slide 13: Module 1 - Introduction to API
13
Data System Designators (DSDs)
D200F is DSD for API
DSDs are assigned to all AFMC software systems
D 200 F
Type of data
(D = materiel management)
Sequentially assigned
Subsystem
Introduction to API

## Slide 14: Module 1 - Introduction to API
14
End of Lesson 1a
Introduction to API

## Slide 15: Module 1 - Introduction to API
15
Lesson 1b
Fundamentals of Configuration Management
Introduction to API

## Slide 16: Module 1 - Introduction to API
16
Lesson Preview
Discusses fundamentals of configuration management and change
Identifies four elements of configuration management
Defines OSS&E
Explains effects of DMSMS on configuration management
Introduction to API

## Slide 17: Module 1 - Introduction to API
17
Configuration Management (CM)
Configuration – the functional and/or physical characteristics of hardware and/or software as set forth in technical documentation and achieved in a product
Primary purpose of CM is to ensure documentation used to identify and describe product and the product itself are one in the same
Identifies change, manages change, ensures changes are properly implemented, reports changes, and records changes
Introduction to API

## Slide 18: Module 1 - Introduction to API
18
Four Elements of CM
Configuration Identification
Configuration Change Control
Configuration Audits
Configuration Status Accounting
Introduction to API

## Slide 19: Module 1 - Introduction to API
19
Configuration Control Board (CCB)
Approves configuration changes
Composed of representatives from program/project functional areas
Approves or disapproves changes via ECPs
Approves conversion of ECPs to TCTOs
Issues implementation instructions
Introduction to API

## Slide 20: Module 1 - Introduction to API
20
OSS&E
Operational Safety, Suitability, and Effectiveness
Do not change configuration, sources of supply, or maintenance concepts for items without approval from engineering
Engineering must approve all part substitutions.
Introduction to API

## Slide 21: Module 1 - Introduction to API
21
DMSMS
The loss, or impending loss, of manufacturers of items or suppliers of items or raw materials (DoD 4140.1-R)
When a part is no longer available due to DMSMS, a substitute must be identified and approved through formal configuration control process
Form, Fit, Function, or Interface
Any configuration change is the alteration of form, fit, function, or interface and could affect the interchangeability and substitutability of an item.
Introduction to API
Notes: DMSMS – Diminishing manufacturing sources materiel shortages

## Slide 22: Module 1 - Introduction to API
22
While Configuration and change control are handled by technical orders (IPB), this data is necessary for the computation of requirements.
Until the day comes when configuration data is systematically fed to the requirements management system, we rely on Equipment Specialists to ensure that our requirements systems are kept up to date.
It’s imperative that requirements system configuration data match IPB information to avoid inaccurate requirements forecasts.
Introduction to API

## Slide 23: Module 1 - Introduction to API
23
End of Lesson 1b
Introduction to API

## Slide 24: Module 1 - Introduction to API
24
Lesson 1c
Interchangeability & Substitutability (I&S)
Introduction to API

## Slide 25: Module 1 - Introduction to API
25
Lesson Preview
Studies Interchangeability & Substitutability (I&S)
Defines Subgroup Master (SGM) item and SGM Stock Number
Describes interchangeables and bachelor items
Explains how requirements are computed for lower subgroups
Introduction to API

## Slide 26: Module 1 - Introduction to API
26
Interchangeability & Substitutability (I&S)
I&S – the conditions which permit the exchange of one item for another without affecting design or performance beyond acceptable limits
I&S Review
Superior to similar items in inventory
Similar to items in inventory
Inferior to items in inventory
Unique (one-of-a-kind)
*More info in AFMCMAN 23-103, Chapter 23
Introduction to API

## Slide 27: Module 1 - Introduction to API
27
Interchangeability & Substitutability (I&S)
I&S determinations are critical to FRL, and to maximize parts supportability
Two essential concepts: Inherent characteristics and form, fit, function, and interface
Inherent Characteristics
Physical and functional qualities which describe an item
Form, fit, function, and interface
Physical and functional qualities of an end-item
Introduction to API

## Slide 28: Module 1 - Introduction to API
28
Interchangeable Items
Equivalent in performance, durability, reliability, and maintainability to another item of similar or identical purposes
Capable of being exchanged without consideration of form, fit, function, and interface, and without alteration of the item or adjoining items (except for adjustment)
Synonymous with inter changeable or two-way interchangeable.
Introduction to API

## Slide 29: Module 1 - Introduction to API
29
Substitutable Items
Two or more items that are similar, but one item has inherent characteristics that make it the preferred item
Capable of being exchanged only under specified conditions or for particular applications
Preferred item can replace the non-preferred item for all applications but not vice versa
Synonymous with the phrase substitutable or one-way interchangeable.
Introduction to API

## Slide 30: Module 1 - Introduction to API
30
Subgroups
Subgroup structure within an I&S group depends on number of items and their interchangeability
Two or more items in same subgroup must be two-way interchangeable items
Preferred item in the subgroup is called the Subgroup Master (SGM)
One-way interchangeables are subgrouped separately and compute separate requirements
API will not permit two members of the same subgroup to be components of the same NHA
Introduction to API

## Slide 31: Module 1 - Introduction to API
31
Order of Use (OOU)
Three-position code is assigned to show ascending order of preference
AAA item first to be made, ACC was the last
Two-way interchangeables share subgroups and the same second digit OOU code
Introduction to API

## Slide 32: Module 1 - Introduction to API
32
Subgroup Master (SGM) Item
Each subgroup contains a SGM
There is an NSN associated with each OOU code, but requirement computations are only made for each SGM
Buys for AA or AB items are rolled to AC automatically
Introduction to API

## Slide 33: Module 1 - Introduction to API
33
Two-Way vs. One-Way
Any item in a subgroup can replace another since they are two-way interchangeables
One-way interchangeables are separate subgroups
A separate indenture structure is built for each subgroup
Introduction to API

## Slide 34: Module 1 - Introduction to API
34
SGM Stock Number
Identifies the most preferred item in an I&S subgroup
I&S Family and I&S Master
I&S family is all subgroups combined
Latest, most preferred item of I&S family is the I&S master
Introduction to API

## Slide 35: Module 1 - Introduction to API
35
Bachelor Item
Item that has no family relationship, no interchangeability
Bachelor stock number is the master stock number for bachelor item
Introduction to API

## Slide 36: Module 1 - Introduction to API
36
I&S Example
Westinghouse
Bachelor Item
SGM and I&S Master
I&S Master
General Electric
Sunbeam
Subgroup A | Subgroup B
AAA - AAB | ABA
Introduction to API

## Slide 37: Module 1 - Introduction to API
37
End of Lesson 1c
Introduction to API

## Slide 38: Module 1 - Introduction to API
38
Lesson 1d
API (D200F) and SPM
Introduction to API

## Slide 39: Module 1 - Introduction to API
39
Lesson Preview
Looks at API’s relationship to the SPM system
Describes API interfaces with SPM and other subsystems
Reviews official API guidance and information sources
Introduction to API

## Slide 40: Module 1 - Introduction to API
40
D200F/API
Subsystem of the D200 RMS
Approved Air Force tool for maintaining hardware indentures and relating program data to secondary items
Purpose of SPM is to compute follow-on spare requirements
Introduction to API

## Slide 41: Module 1 - Introduction to API
41
API and SPM
Purpose of API is to support SPM
API maintains complete indenture structures for all end items
Application programs are input to API and are then used in SPM
API indenture portion also supports DLA, WSSP, AF DMSMS program, and AF depot maintenance activities
Purpose of API interface with SPM, is to update or correct data to the most current information.
Introduction to API
Notes: WSSP –
DMSMS – slide 21

## Slide 42: Module 1 - Introduction to API
42
API Interface with SPM
Mechanized data system that is source of information
API feeds parts and program information to ODS
SPM extracts the information from ODS
API ODS SPM
Introduction to API

## Slide 43: Module 1 - Introduction to API
43
Introduction to API
ODS
SPM

## Slide 44: Module 1 - Introduction to API
44
API Information Resources
Official guidance: AFMCMAN 23-109, “Applications, Programs, and Indentures”
Available at AF E-Publishing website.
Further guidance through AFMC policy letters
and ALC policies and operating instructions
Introduction to API

## Slide 45: Module 1 - Introduction to API
45
End of Lesson 1d
Introduction to API

## Slide 46: Module 2 – Terms and Definitions
46
Lesson 2a
Introduction to Applications, Programs, and Indentures
Module 2 – Terms and Definitions
Terms and Definitions

## Slide 47: Module 2 – Terms and Definitions
47
Lesson Preview
Generally defines Applications, Programs, and Indentures
Terms and Definitions

## Slide 48: Module 2 – Terms and Definitions
48
What are Applications, Programs, and Indentures?
Application – any assembly in an indenture chain that generates measurable program activity
Program – any activity (operating hours, PDM, etc.) that creates the need for spare parts
Indenture – the breakdown of an assembly to its components and the data that defines the relationship of the assembly to its components
Terms and Definitions

## Slide 49: Module 2 – Terms and Definitions
49
Applications
“Application” refers to the NHA involved in the performance of the program
Applications include major end items, major sub-assemblies, or recoverable secondary items
Applications must be maintained
A
M
B
P
Z
D
F
C
G
E
Terms and Definitions

## Slide 50: Module 2 – Terms and Definitions
50
Programs
Programs are operations and activities that create the need for repairs and repair parts
PDM programs are depot-level maintenance programs performed on aircraft, missiles, and trainers
EOH and MISTR programs are depot-level maintenance programs
  Recoverable stock numbers
  TMS
  Support equipment stock numbers
  End-item stock number and Program Element Codes (PEC)
Terms and Definitions

## Slide 51: Module 2 – Terms and Definitions
51
Indentures
Relationships, or “links,” that connect a component to its immediate NHA
Indenture structure relates system/end item to its smallest components
Allow users to trace NHAs or components, and to link NHA components
Relationships maintained by the ES who “owns” the NHA
Imperative to maintain indenture integrity!
Terms and Definitions

## Slide 52: Module 2 – Terms and Definitions
52
End of Lesson 2a
Terms and Definitions

## Slide 53: Module 2 – Terms and Definitions
53
Lesson 2b
Secondary, Recoverable, and Consumable Items
Terms and Definitions

## Slide 54: Module 2 – Terms and Definitions
54
Lesson Preview
Defines secondary, recoverable, and consumable items
Defines NHA and end items
Terms and Definitions

## Slide 55: Module 2 – Terms and Definitions
55
Secondary Items
Component parts that lose identity when installed in an NHA
Installed in higher assemblies or in other recoverable secondary items
Recoverable and consumable items are jointly called secondary items
Terms and Definitions

## Slide 56: Module 2 – Terms and Definitions
56
Recoverable Items
Economically feasible to repair at the depot
Repair costs must not exceed 75% of FUP
Loses individual identity when installed in another piece of equipment
Sometimes referred to as MISTR items
Terms and Definitions
Notes: FUP – Forecasted unit price

## Slide 57: Module 2 – Terms and Definitions
57
Recoverable Item Example
Car Wheel Assembly
When a wheel becomes unserviceable, we could send it to a repair shop.
Parts involved to repair the wheel may include a tire, a rim, valve stem, balance weights, etc.
Terms and Definitions

## Slide 58: Module 2 – Terms and Definitions
58
What is a Next Higher Assembly (NHA)?
The assembly in which a given component is directly installed
What is an end item?
A complete assembly – it has no NHA
Terms and Definitions

## Slide 59: Module 2 – Terms and Definitions
59
Consumable Items
Uneconomical to repair or are consumed in use
Repair costs exceed 75% of FUP
Also lose individual identity when installed in another piece of equipment
Includes items consumed in use such as oil, gasoline, paint, etc. and items that aren’t repairable.
Terms and Definitions

## Slide 60: Module 2 – Terms and Definitions
60
Consumable Item Example
Oil, oil filter, spark plugs, air filter, light bulbs, floor mats, mufflers, speakers, horns, etc.
Terms and Definitions

## Slide 61: Module 2 – Terms and Definitions
61
End of Lesson 2b
Terms and Definitions

## Slide 62: Module 2 – Terms and Definitions
62
Lesson 2c
Identifying Recoverable and Consumable Items
Terms and Definitions

## Slide 63: Module 2 – Terms and Definitions
63
Lesson Preview
Examines code assigned to each federal supply item
Lists different code types and explains purpose of each
Explains repair cost ceiling and its effect
Terms and Definitions

## Slide 64
64
ERRC Codes
Identify item type and management technique
Have two components:
Classify AF items into various management groupings
Found in D043A
C XD1
  ERRC code ERRC designator
Terms and Definitions

## Slide 65: Module 2 – Terms and Definitions
65
ERRC Designator
XD1
1st position – Expendability (E) Designator
Identifies an item as expendable or non-expendable
“X” items are expendable (recoverables and consumables)
“N” items are non-expendable (stand alone end items)
Terms and Definitions

## Slide 66: Module 2 – Terms and Definitions
66
Allowance Standards
Requirements for non-expendable items are based on Allowance Standard (AS) rather than consumption
AS replaces old terminology of Table of Allowance (TA)
AS prescribes the AF equipment items and quantities to perform missions, functions, and duties
AS are available online in the AFEMS
Terms and Definitions
Notes: Requirements for non-expendable items are based on Allowance Standard (AS) rather than consumption
AS replaces old terminology of Table of Allowance (TA)
AS prescribes the AF equipment items and quantities to perform missions, functions, and duties
AS are available online in the AFEMS

## Slide 67: Module 2 – Terms and Definitions
67
ERRC Designator
XD1
2nd position – Reparability and Recoverability (RR) Designator
Identifies items that are recoverable through repair or are not normally subject to repair
Also designates level of repair or condemnation of an IOS:
  B – not subject to repair or consumed in use
  D – subject to repair and should be returned to depot or specialized repair activity
  F – authorized to be repaired at organizational and intermediate levels
Not intended to dictate maintenance policy but to avoid over management of low price items (SMR codes dictate maintenance policy)
Terms and Definitions

## Slide 68: Module 2 – Terms and Definitions
68
ERRC Designator
XD1
3rd position – Category (C) Designator
Identifies items to be given intensified or specialized attention
Items designated “1” are important to track
  SCARS is technique for intensive management
Items designated “2” do not fall under intensified or specialized management
Items designated “3” are EOQ items (normally thrown away)
Terms and Definitions

## Slide 69: Module 2 – Terms and Definitions
69
ERRC Code Table
Terms and Definitions

## Slide 70: Module 2 – Terms and Definitions
70
Repair Costs and ERRC Codes
If repair costs exceed 75% FUP, the ES or Engineer reviews item for possible ERRC code change
Terms and Definitions

## Slide 71: Module 2 – Terms and Definitions
71
SMR Codes
Assigned to all items that make up a system or equipment
Mandatory entry to establish an indenture in API
Portray maintenance decisions made by the ES:
  Repair level responsibilities
  Support methods
  Disposition instructions
  Reside in the IPB
Is the ES’s responsibility to update as necessary
Terms and Definitions

## Slide 72: Module 2 – Terms and Definitions
72
SMR Code Example
PAOLD
P=Procurable
A=Stocked
O=Remove and Replace at the Organizational Level
L=Depot Level Repair (organic and/or contract)
D=Reparable Condemned by Depot Only
Terms and Definitions

## Slide 73: Module 2 – Terms and Definitions
73
Proper SMR coding
Reduces part number requisitions
Enhances logistics support
SMR codes may require revision after systems are in operational use or when new repair/support decisions are made
See TO 00-25-195 for more SMR code info
Terms and Definitions

## Slide 74: Module 2 – Terms and Definitions
74
SMR and ERRC Code Compatibility
Single position ERRC code is added to end of five position SMR code
ERRC code is a separate field in API
SMR codes should remain compatible with the ERRC code
Incompatibility demands that one or both be updated.
ES establishes ERRC and SMR codes
Terms and Definitions

## Slide 75: Module 2 – Terms and Definitions
Terms and Definitions

## Slide 76: Module 2 – Terms and Definitions
76
End of Lesson 2c
Terms and Definitions

## Slide 77: Module 2 – Terms and Definitions
77
Lesson 2d
National Stock Number (NSN)
Terms and Definitions

## Slide 78: Module 2 – Terms and Definitions
78
Lesson Preview
Discusses NSNs and elements that make up an NSN
Examines FSC, NIIN, NCB, and MMAC
Terms and Definitions

## Slide 79: Module 2 – Terms and Definitions
79
Nouns and Part Numbers
A noun is name of the object (oil pump, valve assembly, etc.)
For file maintenance and indentures, a noun is the name of the item
A part number is a combination of numbers, letters, and symbols assigned by a designer, a manufacturer, or a vendor
Two or more completely different parts can be assigned the same part number
Terms and Definitions

## Slide 80: Module 2 – Terms and Definitions
80
Commercial and Government Entity (CAGE) Codes
Five position code assigned to identify manufacturer
CAGE codes must always accompany part numbers in API
May also be referred to as Federal Supply Codes for Manufacturers (FSCM)
Terms and Definitions

## Slide 81: Module 2 – Terms and Definitions
81
What is a National Stock Number?
National Stock Number (NSN) identifies each item of supply
Assigned to each supply item purchased, stocked, or distributed
Can be 13 or 15 digits
Terms and Definitions

## Slide 82: Module 2 – Terms and Definitions
82
First four digits of NSN are the FSC
FSC identifies the supply classification of an item
Assigned based on the item noun IAW DLA H2 handbook
Terms and Definitions

## Slide 83: Module 2 – Terms and Definitions
83
Next nine digits are the NIIN
NIIN differentiates individual supply items
Within NIIN is the NCB code (first two digits)
Terms and Definitions

## Slide 84
84
NCB identifies country that cataloged item
US items have NCB of 00 or 01
Terms and Definitions

## Slide 85: Module 2 – Terms and Definitions
85
Remaining seven digits of NIIN are unique FLIS identification numbers
NIIN stays with item while it is in supply
API indentures by part number/CAGE, not NIIN
Terms and Definitions

## Slide 86
86
15 digit NSNs contain the MMAC code
Two-position MMAC identifies:
  Items used on only one weapon system
  Special items that require special management
  Items managed by someone other than FSC manager
All non-DLA items have MMAC codes
Terms and Definitions

## Slide 87: Module 2 – Terms and Definitions
87
NSNs determine location of management responsibility
MMAC code always takes precedence over FSC
Terms and Definitions

## Slide 88: Module 2 – Terms and Definitions
88
End of Lesson 2d
Terms and Definitions

## Slide 89: Module 3 – Applications, Programs, and Indentures
89
Lesson 3a
Applications
Applications, Programs and Indentures

## Slide 90: Module 3 – Applications, Programs, and Indentures
90
Lesson Preview
Looks at relationship of applications to indentures and programs
Outlines ES responsibilities for applications
Applications, Programs and Indentures
Notes: - API is where programs are distributed to secondary components, allows for relationships to be established between items and end items where programs are computed for SPM

## Slide 91: Module 3 – Applications, Programs, and Indentures
91
Applications Define Relationships
Applications portion of API distributes programs to secondary components
Applications portion defines relationship between components and higher assemblies that generate programs
Applications, Programs and Indentures
Notes: - Defines relationship between components and the higher assemblies, it relates aerospace vehicles, equipment, engines and other end items to operational, inventory, and maintenance program data

## Slide 92: Module 3 – Applications, Programs, and Indentures
92
Program Selection
Assigns program data from application to components
Allows automated and manual linkage of components to applications
Each component must have at least one application to compute requirements
Program data are directly assigned to each application
Data elements unique to each application determine how much program to assign to each component
Applications, Programs and Indentures
Notes: - API program selection allows linking of components to their application, and you have to have at least one application in order to compute requirements

## Slide 93: Module 3 – Applications, Programs, and Indentures
93
ES Application Responsibilities
Ensures that indentures and application data are complete and accurate
File maintains all needed applications into API
File maintains each item’s Program Selection record
Applications, Programs and Indentures
Notes: -As the ES, you ensure complete and accurate indenturing
- AFMCMAN 23-101

## Slide 94: Module 3 – Applications, Programs, and Indentures
94
End of Lesson 3a
Applications, Programs and Indentures

## Slide 95: Module 3 – Applications, Programs, and Indentures
95
Lesson 3b
Programs
Applications, Programs and Indentures

## Slide 96: Module 3 – Applications, Programs, and Indentures
96
Programs
Lesson Preview
Studies nine program types employed by applications
Identifies programs used most frequently
Explains purpose of application programs
Explains how past and future programs are used
Defines item installed program and explains how they’re computed
Lists sources for each program type
Applications, Programs and Indentures

## Slide 97: Module 3 – Applications, Programs, and Indentures
97
Programs
Types of Programs Employed by Applications
Specific programs are activities which create the need for repair parts, maintenance, or overhauls
Eight different program types used in requirements computations
Applications, Programs and Indentures

## Slide 98: Module 3 – Applications, Programs, and Indentures
98
Programs
Program Types
Type 1: Operating Hours
Hourly programs include flying hours and equipment operating hours
Hourly programs expressed in 100 hour increments (345 hours on factors printout means item operated for 34,500 hours)
Type 3: Inventory or Equipment Months
Average number of end items in inventory for a given month multiplied by three
30 equipment months for Q1 = 10 units per month
Applications, Programs and Indentures

## Slide 99: Module 3 – Applications, Programs, and Indentures
99
Programs
Program Types (cont.)
Type 4: Program Depot Maintenance (PDM)
Number of scheduled depot level overhauls of an application
Excludes XD1, XD2, and ND2
Type 5: Sorties
Represents sorties, or the number of takeoffs and landings for the aircraft
More efficient computations for certain types of equipment (tires, landing gear, etc.)
Type 6: Engine Overhaul (EOH)
Number of scheduled depot level overhauls of an engine
Applications, Programs and Indentures

## Slide 100: Module 3 – Applications, Programs, and Indentures
100
Programs
Program Types (cont.)
Type 7: Drone Recoveries
Equal to launches minus expenditures
Type 8: Ammunition Expenditures
Number of rounds fired, or expected to be fired, through weapon
Displayed in thousands of units for future programs; actual numbers for past quarters
Type 9: NHA MISTR
Repairing NHAs creates a repair program for its components
NHA MISTR are depot level maintenance programs pertaining to recoverable or support equipment stock number applications
Equal to actual depot overhaul repair or reparable assets that have been made serviceable during MISTR repair process
Applications, Programs and Indentures

## Slide 101: Module 3 – Applications, Programs, and Indentures
101
Programs
Two Categories of Programs
Organizational and Intermediate Maintenance (OIM) programs
  Activities at operational user’s level
  Types: operating hours, equipment months, sorties, drone recoveries, ammunition expenditures
Depot Level Maintenance (DLM) programs
  Activities during end item overhaul or higher assembly depot level repair
  Types: PDM, EOH, NHA MISTR
Applications, Programs and Indentures

## Slide 102: Module 3 – Applications, Programs, and Indentures
102
Programs
Program Data Example
Applications, Programs and Indentures
OIM Type
Hours
Equipment Months
Sorties
Drone Recoveries
Ammo Expenditures
DLM Type
PDM
EOH
NHA MISTR

## Slide 103: Module 3 – Applications, Programs, and Indentures
Used to compute the OIM, PDM, EOH, and NHA MISTR rates and percents (factors)
The program performed by the item
Term used throughout requirements computations
Must be forecastable
ES determines type of item program to be developed and ensures input to API
103
Programs
What is an item program?
How are past item programs used?
Applications, Programs and Indentures

## Slide 104: Module 3 – Applications, Programs, and Indentures
Program performed or to be performed by item while installed
Used to compute projected requirements
ES is responsible to ensure correct applications are input to API
104
Programs
How are future item programs used?
What is an item installed program?
Applications, Programs and Indentures

## Slide 105: Module 3 – Applications, Programs, and Indentures
105
Programs
Sources of Application Programs
HQ AFMC, System Program Managers, Engine Managers, Inventory Managers
Applications, Programs and Indentures

## Slide 106: Module 3 – Applications, Programs, and Indentures
106
End of Lesson 3b
Programs
Applications, Programs and Indentures

## Slide 107: Module 3 – Applications, Programs, and Indentures
107
Lesson 3c
Indentures
Applications, Programs and Indentures

## Slide 108: Module 3 – Applications, Programs, and Indentures
108
Indentures
Lesson Preview
Defines indenture chains and indenture levels
Explains how indenture structure relates to the IPB
Describes ES responsibilities for maintaining indenture structures
Applications, Programs and Indentures

## Slide 109: Module 3 – Applications, Programs, and Indentures
109
Indentures
Indenture Chain
One or more indenture relationships showing an end item’s relationship to the smallest component
Allows users to trace NHA or lower assembly components and link NHA components together
Building a full indenture chain may require several ES’s at different ALCs
No limit to number of indentures that can form an indenture chain
Applications, Programs and Indentures

## Slide 110: Module 3 – Applications, Programs, and Indentures
110
Indentures
Indenture Level
Level of the component or assembly (highest level is system, lowest is component)
Used within an indenture chain to denote distance of items
Applications, Programs and Indentures

## Slide 111: Module 3 – Applications, Programs, and Indentures
111
Indentures
Indenture Example
Applications, Programs and Indentures

## Slide 112: Module 3 – Applications, Programs, and Indentures
112
Indentures
Indentures and IPBs
Indentures should reflect the IPBs in the -4 series of TOs
IPB provides instructions for identifying and requisitioning parts and illustrates assembly and disassembly
Indenture structure is like IPB structure
Applications, Programs and Indentures

## Slide 113: Module 3 – Applications, Programs, and Indentures
113
Indentures
Indenture and IBP structure example
Indenture IPB (-4 TO)
Applications, Programs and Indentures

## Slide 114: Module 3 – Applications, Programs, and Indentures
114
Indentures
Indenture Relationships Maintained by the ES
Indenture integrity must be maintained
Indenture records through automated API interface and manual input
ESs, ALC OPRs, and HQ AFMC analysts may update indenture records
Only responsible ES may add, change, or delete data for specific component or subassembly
ESs must ensure changes to indenture structures are reflected in API
ESs must correct inaccurate indenture structures
Applications, Programs and Indentures

## Slide 115: Module 3 – Applications, Programs, and Indentures
115
End of Lesson 3c
Indentures
Applications, Programs and Indentures

## Slide 116: Module 3 – Applications, Programs, and Indentures
116
Lesson 3d
The Illustrated Parts Breakdown (IPB)
Applications, Programs and Indentures

## Slide 117: Module 3 – Applications, Programs, and Indentures
117
Lesson Preview
Looks at IPB as authoritative source for indenture information
Applications, Programs and Indentures

## Slide 118: Module 3 – Applications, Programs, and Indentures
118
Illustrated Parts Breakdown (IPB)
Part - component relationships
Identification and requisitioning of parts
Identification of item management methods, shipping requirements, etc.
Defines types of stock
Does not provide maintenance or assembly instructions
Applications, Programs and Indentures

## Slide 119: Module 3 – Applications, Programs, and Indentures
119
Applications, Programs and Indentures

## Slide 120: Module 3 – Applications, Programs, and Indentures
120
End of Lesson 3d
Applications, Programs and Indentures

## Slide 121: Module 4 – API Subsystem
121
Lesson 4a
Application Data
API Subsystem

## Slide 122: Module 4 – API Subsystem
122
Lesson Preview
Defines various application data elements:
  Standard Program Designator (SPD)
  Program Select Code (PSC)
  Program Development Code (PDC)
  Program Begin Date (PBD)
  Quantity Per Application (QPAPPL)
  Application Percent (APPL%)
API Subsystem

## Slide 123: Module 4 – API Subsystem
123
Application Data is Vital
Application data is foundation of
Requirements planning
Application data is vital to conversion
of application programs to item
programs
Application data must be complete and accurate
Each application must be established in API
ES must file maintain application data
Accurate info can be obtained from historical records or TOs
API Subsystem

## Slide 124: Module 4 – API Subsystem
124
Component Item Review List
A source of application data
Information can be used to identify end item applications
Contains information from all ALCs
Can be verified with IPB, TO, or drawings
Requested by ES on an as needed basis
API Subsystem

## Slide 125
125
API Application Format
Must be typed onscreen exactly, including leading spaces
Unique combination of 25 letters, spaces, numbers assigned to NHA
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | …
MDS |  | K | C | 1 | 3 | 5 | R |  |  |  |  |  |  |  |  |  |  |  |  |  | 
TMS |  | T | F | 0 | 0 | 3 | 0 | 1 | 0 | 3 |  |  |  |  |  |  |  |  |  |  | 
Missile | A | G | M | 0 | 8 | 6 | B |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Drone |  | Q | F | 1 | 0 | 6 | B |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Trainer | 1 | A | D | 0 | 0 | 0 | A |  |  |  |  |  |  |  |  |  |  |  |  |  | 
NSN | 0 | 1 | 5 | 6 | 4 | 8 | 5 | 7 | 3 |  |  |  |  |  |  |  |  |  |  |  | 
PEC | 5 | 6 | 0 | 1 | 3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
MOD |  |  | B | 0 | 5 | 2 | H |  |  |  |  |  | R | F | 4 | 5 | 3 | 2 | 4 | A | 
Module 4 – API Subsystem
API Subsystem

## Slide 126: Module 4 – API Subsystem
126
Application Data Elements
Standard Program Designator (SPD)
Program Select Code (PSC)
Program Development Code (PDC)
Program Begin Date (PBD)
Quantity Per Application (QPAPPL)
Application Percent (APPL%)
API Subsystem

## Slide 127: Module 4 – API Subsystem
127
Standard Program Designator (SPD)
Application = SPD
SPD is end item or assembly that generates programs
SPD becomes application when one or more components have been selected to receive program data from that SPD
Each application must be established in API as an SPD
SPD can be up to 25 characters long
API Subsystem

## Slide 128: Module 4 – API Subsystem
128
Types of SPDs
A = Aircraft
C = Communication/Electronic/Meteorological (CEM)
D = Engine Module
E = Engine
G = Gun
L = Communication/Electronic Network
M = Missile
P = Program Element Code
Q = Support Equipment
R = Drone
T = Trainer
V = Support Equipment (Vehicle)
X = Auxiliary Power Unit (APU)
Z = Modification Designation
API Subsystem

## Slide 129: Module 4 – API Subsystem
129
Program Select Code (PSC)
Selects type of program used in requirements computations
Two position code
ES can file maintain one OIM, one DLM program type per application
1st Position (OIM) | 2nd Position (DLM)
0 – No OIM program | 0 – No DLM program
1 – Operating hours | 4 – Programmed Depot Maintenance (PDM)
3 – Equipment months | 6 – Engine Overhaul (EOH)
5 – Sorties | 9 – NHA MISTR
7 – Drone recoveries | 
8 – Ammunition expenditures | 
API Subsystem

## Slide 130: Module 4 – API Subsystem
130
Program Development Code (PDC)
Manually file maintained in application data record
Allows ES to determine which program is to be used in requirements computation: past program, future program, or both
Field usually blank (system develops both past and future programs)
API Subsystem

## Slide 131: Module 4 – API Subsystem
131
Program Begin Date (PBD)
Describes when an item became operational on an application
Starting point for computing an item program
Field reflects last month of quarter when component was first installed on SPD
Quarter expressed in YYYY/MM format: June 1985 = 1985/06
Only 03, 06, 09, and 12 acceptable in quarter column
PBD required by API
Cannot be file maintained as 0000 or left blank
API Subsystem

## Slide 132: Module 4 – API Subsystem
132
Quantity Per Application (QPAPPL)
Maximum quantity of item installed on the application
Should never be zero
Should not be confused with Quantity Per Assembly (QPA)
API Subsystem

## Slide 133
133
Application Percent (APPL%)
Percentage of higher assemblies that have a component installed
API assigns 100% as default percent for each component-application
ES can change APPL% in API Program Selection function
Most common reason to change APPL% is to reflect mod schedule
Displayed as “Override Application Percent” when changed by ES
ES responsibility to know and maintain correct APPL%
API Subsystem

## Slide 134
134
End of Lesson 4a
API Subsystem

## Slide 135: Module 4 – API Subsystem
135
Lesson 4b
Establishing Indenture Records
API Subsystem

## Slide 136: Module 4 – API Subsystem
136
Lesson Preview
Covers indenture record establishment
API Subsystem

## Slide 137: Module 4 – API Subsystem
137
Record Establishment
ESs, ALC OPRs, and HQ AFMC analysts may update indenture records
Only responsible ES may add, change, or delete data for particular component or assembly
API Subsystem

## Slide 138: Module 4 – API Subsystem
138
Automated Data Sources
Contractor Data
Provisioning
API Subsystem

## Slide 139: Module 4 – API Subsystem
139
Contractor Data
AF acquires indenture records from manufacturers
Records are complete indenture files in electronic form
Formats and procedures in AFMCMAN 23-109, Chapter 7
API Subsystem

## Slide 140: Module 4 – API Subsystem
140
Provisioning
Creates indenture records through interface with D220
D220 produces indenture file that reflects PPL
You should manually add any missing indentures
You must ensure accuracy of indentures before passing
them to API
API Subsystem
Notes: PPL –provisioning parts list

## Slide 141: Module 4 – API Subsystem
141
Manual Data Sources
Online system
Primary sources
  IPB in –4 TOs
  Technical manuals
  Provisioning documents
API Subsystem

## Slide 142: Module 4 – API Subsystem
142
Other Sources
API automatically establishes indenture records when components without a record are replaced
API places “V” in SID code area, and “REVIEW” in BSN field of indenture screen
ES reviews the indenture and either accepts the change by adding a review date, or adds the correct indenture information
New Components for Existing NHA product advises you of condition
Review product and use it to build or change records
API Subsystem

## Slide 143
143
Indenture Data Sustainment
You are responsible for maintaining indenture data within API for the life of the system or end item
Incorporate any changes within API
File maintain review dates!
NHA review dates can’t be over 18 months old.
Change processes:
  Notifications
  Design changes
  Cataloging actions
  Component replacement usage
  TO actions
  SMR codes
  Repair programs
API Subsystem

## Slide 144: Module 4 – API Subsystem
144
End of Lesson 4b
API Subsystem

## Slide 145: Module 4 – API Subsystem
145
Lesson 4c
Fundamental Indenture Terms and Formulas
API Subsystem

## Slide 146: Module 4 – API Subsystem
146
Lesson Preview
Covers fundamental indenture terms and formulas
API Subsystem

## Slide 147: Module 4 – API Subsystem
147
Production History
Number of end items that were repaired
Includes:
  PDM
  EOH
  Depot repair of NHA recoverable end item
API Subsystem

## Slide 148: Module 4 – API Subsystem
148
Consumption History
Materials consumed to accomplish the repair
Cannot be consumption history without production history
Includes:
  Consumption quantity
  Consumption date
  Source of repair
Date and source of repair must match NHA production
Production and consumption history indicate future needs
Keep separate consumption records for components used in the repair of multiple NHAs
API Subsystem

## Slide 149: Module 4 – API Subsystem
149
Indenture Replacement Percent (REPL%)
Identifies how often a component is removed and replaced
Used within single level of indenture
Consumption History
X 100 = REPL%
Production History X QPA
API Subsystem

## Slide 150: Module 4 – API Subsystem
150
REPL% Examples
Example 1) Outboard Wheel Half on C-5 is being replaced during the MISTR repair of the Wheel 37% replacement rate minus 10% for fixing fatigue cracks equals a 27% replacement rate is file maintained as estimate by the ES
Example 2) Replacement percent for valve packing
Maximum REPL% in API is 125 percent (default is 0 %)
45
X 100 = REPL% of 90
50 X 1
API Subsystem

## Slide 151: Module 4 – API Subsystem
151
Derived Replacement Percent
Considers all indenture levels between component and application
Consumption History
X 100 = Derived REPL%
Production History X QPAPPL
API Subsystem

## Slide 152: Module 4 – API Subsystem
152
Override Replacement Percent (OVRD REPL%)
ES estimate of replacement percent
Can only be assigned with N, P, C, or T ERRC codes
Only used for Materiel Requirements List (MRL) or Purchase Request Support List (PRSL)
API Subsystem

## Slide 153: Module 4 – API Subsystem
153
Replacement Percent Source Reference Code (SRC)
Displays the source of the replacement percent
Blank with two or more indenture levels
Possible SRC codes:
  A = actual
  C = computed or computer assigned
  E = entered
  S = standard (default value)
  D = contractor quotes
  P = peacetime values in OWRM computation
  W = wartime values in OWRM computation
  F = not entered during initial indenture establishment
API Subsystem

## Slide 154: Module 4 – API Subsystem
154
Quantity Per Assembly (QPA)
Number of components installed on the immediate NHA
File maintained by ES in API
Do not confuse with QPAPPL
API Subsystem

## Slide 155: Module 4 – API Subsystem
155
Derived Quantity Per Application (QPAPPL)
Total number of components per NHA/SPD
Derived QPAPPL is mechanically computed by API
2 X 2 X 1 = QPAPPL of 4
API Subsystem
Notes: SPD – System programming designator

## Slide 156: Module 4 – API Subsystem
156
QPAPPL for Multiple Chains
C-D = 1
C-G-D = 8
C-G-J-D = 6
1 + 6 + 8 = QPAPPL of 15
API Subsystem

## Slide 157
157
Override Quantity Per Application (OVRD QPAPPL)
ES can change QPAPPL in Program Selection function
Changed values displayed as “OVRD QPAPPL”
ES must manually enter OVRD QPAPPL by Time Phase Date when changes to QPAPPL are anticipated (e.g., modifications)
API Subsystem

## Slide 158: Module 4 – API Subsystem
158
Application Percent (APPL%)
Tells API what percent of NHA has component installed
Most common APPL% is 100 (default value)
Override Application Percent (OVRD APPL%)
ES can override APPL% by entering value greater than zero
ES uses program selection function to override APPL%
Changed value displayed as OVRD APPL%
API Subsystem

## Slide 159: Module 4 – API Subsystem
159
End of Lesson 4c
API Subsystem

## Slide 160: Module 4 – API Subsystem
160
Lesson 4d
Output Products
API Subsystem

## Slide 161: Module 4 – API Subsystem
161
Lesson Preview
Covers output products ES can obtain from API system
API Subsystem

## Slide 162: Module 4 – API Subsystem
162
Output Products
Indenture structure is source for output products
Three categories of output products:
  User requested (“pull”)
  System generated (“push”)
  Batch processes
Push and pull products through CA DISPATCH
API Subsystem

## Slide 163: Module 4 – API Subsystem
163
CA Dispatch
Access to API products is available through CA Dispatch software package
Every report in CA Dispatch is identified by a job name in format of DBPXXXAA:
  1) DBP = DBP is constant
  2) XXX = the last three characters of your user ID
  3) AA = a sequential alpha designator from AA to ZZ
  Example: DBPSGMLV
API will direct push products directly to user ID of product owner; pull products must be requested, then retrieved by user ID of requester
API Subsystem

## Slide 164: Module 4 – API Subsystem
164
Push Products
Automatically generated by systems
API Subsystem

## Slide 165: Module 4 – API Subsystem
165
Selected Items for Review List
Lists all recoverable items currently computing a repair requirement for which there is no NHA record reviewed within past 12 months
Generates quarterly from ALC repair schedule
Any items not resident and reviewed within past 12 months are tagged for review
ES must review indenture data for NHA and components for accuracy and update as necessary
ES must establish current review date. Can’t be > 18 months old.
Review date is ES signature
API Subsystem

## Slide 166: Module 4 – API Subsystem
166
Incomplete Indenture Chain Report (IIC)
API does quarterly comparison of applications to indentures
IIC allows users to compare physical relationships to program selection relationships to identify missing indentures
If indenture chain does not exist from SPD to component, report generates to ES of SPD and SPD is identified
If SPD does not exist as NHA in indenture, or indenture chain does not exist, report generates to ES of component and component is identified
Two parts to report: part 1 lists SPD applications that are not NHA, part 2 lists SPD applications that are NHA but don’t have a chained relationship to the component NIIN/TMS
API Subsystem

## Slide 167: Module 4 – API Subsystem
167
Review Update Suspense Notice
Notifies ES of request for list of components needed to repair a NHA
Identifies NHA for which component data was requested
One of three messages will appear in report
  1) “Initial Bill of Materials Provided. FRL and REA Produced for Review and Update of Relationships.”
  2) “Item Exempt Coded. Requestor notified. Research Exempt Coded Items to Insure Properly Coded.”
  3) “NHA Does Not Exist.”
Components remain in system until ES deletes them, or adds or changes information to complete the relationship
API Subsystem

## Slide 168: Module 4 – API Subsystem
168
New NHAs and Related Components
ES receives report when maintenance reports repair of NHA that is not identified as a NHA in API
Includes NHA that was repaired and a list of components consumed during repair
If ES determines relationship is valid, he or she must establish the NHA - component relationship in API
If relationship data is inaccurate, the repair facility should be notified
API Subsystem

## Slide 169: Module 4 – API Subsystem
169
New Components for Existing NHA
ES receives report when maintenance reports component consumption during NHA repair, and there is no relationship of that component to NHA in API
Purpose of report is to advise managing ES of NHA that components on report have been added to the indenture record in API
“V” SID code will appear on indentures screen, as well as “REVIEW” in the BSN field
ES should review report and verify that new indentures are valid (or reconcile existing indentures with the report)
ES may need to coordinate with maintenance activity to verify
API Subsystem

## Slide 170: Module 4 – API Subsystem
170
Component Items for Review – Action
Contains all “incomplete relationships” as of the date that the report is generated
All components in this report have previously appeared in New Components for Existing NHA report
Reminds ES of an invalid condition that must be verified or deleted
API Subsystem

## Slide 171: Module 4 – API Subsystem
171
API Subsystem

## Slide 172: Module 4 – API Subsystem
172
Component Item Review List (CIRL)
Displays all NHAs for specified component
Useful for locating NHAs affected by defective components or DMSMS
Displays NHA production, consumption, REPL%, and SRC
API Subsystem

## Slide 173: Module 4 – API Subsystem
173
Full Range List (FRL)
Displays all components indentured to NHA
Several ways to request report:
  By NHA – enter part number and CAGE, enter “Y” in all levels
  Only first level components – enter “N” in all levels
  By ES managing NHA – enter only ALC, pseudo-division code, and ES code
API Subsystem

## Slide 174: Module 4 – API System
174
API Subsystem

## Slide 175: Module 4 – API Subsystem
175
Indenture Chains (All)
Displays all indenture chains that exist for a component
Request by specifying NIIN, part number/CAGE, or TMS
If component is link in multiple chains, each indenture chain listed on separate page
API Subsystem

## Slide 176: Module 4 – API Subsystem
176
Indenture Structure Top-Down
Displays NHA and its components from top to bottom
Similar to FRL but excludes tools, test equipment, bulk materials, parts kits, and TOs
May view all components or limit to components with C, P, S, and T ERRC codes
Request by entering NIIN, SPD, or part number/CAGE
API Subsystem

## Slide 177: Module 4 – API System
177
API Subsystem

## Slide 178: Module 4 – API Subsystem
178
Material Requirements List (MRL)
Displays all components of NHA and repair quantity needed
Last section displays investment and expense cost information
May include all components or recoverable items only
Required to support contract maintenance
Components on list must have:
  NIIN, or have a source code of AD or MD
  REPL% greater than zero
  Special Identification Designator other than D, E, F, G, L, R, or T
User may also request BML with this list
API Subsystem

## Slide 179: Module 4 – API Subsystem
179
Bulk Materials List (BML)
Contains all components of a specified NHA with SID L (bulk material)
If “Recoverables Only” option is selected, the report will give all levels of bulk materials to point in each chain when a component is ERRC coded C, T, S, U, or a Standard Designator (unless component is SID coded W)
Each occurrence of a bulk material item within indenture structure will be included on a separate component line
Cannot be obtained without the MRL
API Subsystem

## Slide 180: Module 4 – API System
180
API Subsystem

## Slide 181: Module 4 – API Subsystem
181
NHA by ES (NBES)
Displays every NHA in API assigned to a given ES code
Excellent report to review indentures and exempt-coded items for each ES
API Subsystem

## Slide 182: Module 4 – API Subsystem
182
NHAs with Indenture Suppress Indicator On (RSPI)
NHAs appear on this report when they meet these conditions:
  Indenture Suppress Indicator equals “Y”
  Review Date is within the requested range or within the default range
  ALC matches the ALC in the selection criteria
  If specified, the DIV and ES match those selected by the requestor
Report will indicate that Indenture Suppress Indicator of those NHAs having a Review Date older than 18 months will be reset at next monthly report
API Subsystem
Notes: RSPI - ???

## Slide 183
183
Purchase Request Support List (PRSL)
Allows one MRL report for multiple NIINs (10 maximum).
Components on list must have:
  NIIN, or have a source code of AD or MD
  REPL% greater than zero
  Special Identification Designator other than D, E, F, G, L, R, or T
Three parts:
  Part 1 lists NSNs to be repaired
  Part 2 lists components and quantities required to repair part 1 items
  Part 3 sums cost data for part 2 component quantities
API Subsystem

## Slide 184: Module 4 – API Subsystem
184
Repair Experience Analysis (REA)
Displays repaired item with production history and all components with consumption history for item
Lists same components as Indenture Structure Top-Down
Reason codes are:
  A – report was requested by user
  B – report was generated as result of BOM being requested through G005M
Can request report for all NHAs assigned to specific ES
API Subsystem

## Slide 185
185
Repair Experience Analysis (REA)
Displays repaired item with production history and all components with consumption history for item
Lists same components as Indenture Structure Top-Down
Reason codes are:
  A – report was requested by user
  B – report was generated as result of BOM being requested through G005M
Can request report for all NHAs assigned to specific ES
API Subsystem

## Slide 186: Module 4 – API Subsystem
186
ESD Identification Product (RESD)
Displays all components with ESD designator
Indent Chain-Specified NHA (RICS)
Displays all indenture chains between specified NHA and component
Special ID Designator (RSID)
Displays all components of a specified NHA that are assigned a SID
Can be used to list all shop manufactured items (SID M), repair parts/kits (SID S), tech orders (SID T), or G005M parts (SID V)
API Subsystem

## Slide 187: Module 4 – API Subsystem
187
Exempt Code Query (RXMT)
Displays all NHA identities for specified exempt code
Tools and Test Equipment (TTE)
Identifies and describes TTE necessary to repair NHA
May view all component levels by leaving “Recoverables Only” field blank
Entering “Y” produces all component levels to point where reparable component is noted
API Subsystem

## Slide 188: Module 4 – API Subsystem
188
End of Lesson 4d
API Subsystem

## Slide 189: Module 4 – API Subsystem
189
Lesson 4e
API File Maintenance (FM) Screens
API Subsystem

## Slide 190: Module 4 – API Subsystem
190
Lesson Preview
Covers API file maintenance screens
API Subsystem

## Slide 191: Module 4 – API Subsystem
191
API User Groups
  Equipment Specialists (ES)
  HQ AFMC Indenture OPR
  HQ AFMC Program OPR
  HQ AFMC MMM RDB Policy OPR
  HQ AFMC Reclamation OPR
  ALC Indenture Monitor
  ALC Program Monitor
  Systems Program Manager (SPM)
  Production Management Specialist (PMS)
  Reclamation Program Control Officer (RPCO)
Only ES can file maintain indentures
ES must be owner of higher assembly/end item
API Subsystem

## Slide 192: Module 4 – API Subsystem
192
File Maintenance
API Subsystem

## Slide 193: Module 4 – API Subsystem
193
Copy/Add Indenture (CAI)
API Subsystem

## Slide 194: Module 4 – API Subsystem
194
Change of Program Select Code (CHPS)
API Subsystem

## Slide 195: Module 4 – API Subsystem
195
Consumption History (CONS)
API Subsystem

## Slide 196: Module 4 – API Subsystem
196
Next Higher Assembly (NHA)
API Subsystem

## Slide 197: Module 4 – API Subsystem
197
NHA Exempt Codes
API Subsystem

## Slide 198: Module 4 – API Subsystem
198
Production History (PROD)
API Subsystem

## Slide 199: Module 4 – API Subsystem
199
Program Selection (PS)
API Subsystem

## Slide 200: Module 4 – API Subsystem
200
End of Lesson 4e
API Subsystem

## Slide 201: Module 4 – API Subsystem
201
Lesson 4f
Indenture (IND) Screen in File Maintenance
API Subsystem

## Slide 202: Module 4 – API Subsystem
202
Lesson Preview
Reviews procedures for entering and modifying indenture records in API
API Subsystem

## Slide 203: Module 4 – API Subsystem
203
API Subsystem

## Slide 204: Module 4 – API Subsystem
204
New Indenture Walkthrough
API Subsystem

## Slide 205: Module 4 – API Subsystem
205
New Indenture Walkthrough
Step 1) Access Indentures screen
Step 2) Select Blank function to clear existing data from screen
API Subsystem

## Slide 206: Module 4 – API Subsystem
206
Function Codes
API Subsystem

## Slide 207: Module 4 – API Subsystem
207
NHA Information
Step 3) Enter the Cartridge Assembly as the NHA
New indentures must be added by part number/CAGE not NIIN
API Subsystem

## Slide 208: Module 4 – API Subsystem
208
NHA Data
Step 4) Enter Identification Plate as component
Step 5) Select (A) in the Function field to add new indenture
Step 6) If necessary, confirm entry of NHA and component
Step 7) Enter the SMR Code for the NHA
API Subsystem

## Slide 209: Module 4 – API Subsystem
209
NHA Data
SMR code is mandatory entry when establishing indenture
Review date indicates when NHA in relationship was last reviewed (entered on NHA screen)
Review includes ensuring all component parts are properly indentured and all indenture data is valid and current
ERRC code can only be changed through a cataloging action
Name part established through cataloging
API Subsystem

## Slide 210: Module 4 – API Subsystem
210
Component Data
Step 8) Enter the SMR code
Step 9) Enter the QPA
Step 10) Enter the Subsystem and Item Essentiality Codes
API Subsystem

## Slide 211: Module 4 – API Subsystem
211
Essentiality Codes
ES has responsibility to file maintain three position MIEC for each application record in API
MIEC has three positions/components:
1) System Essentiality Code (SEC)
2) Subsystem or Equipment Essentiality Code (SSEC)
3) Item Essentiality Code (IEC)
API Subsystem

## Slide 212: Module 4 – API Subsystem
212
API Subsystem

## Slide 213: Module 4 – API Subsystem
213
API Subsystem

## Slide 214: Module 4 – API Subsystem
214
API Subsystem

## Slide 215: Module 4 – API Subsystem
215
Special Identification Code (SID)
One objective of API is to provide repair information for special resources
Everything required for depot repair of NHA must be indentured
SID provides a method to identify resources as components in the indenture that are non-standard parts
API Subsystem

## Slide 216: Module 4 – API Subsystem
216
API Subsystem

## Slide 217: Module 4 – API Subsystem
217
Electrostatic/Electromagnetic Sensitive Devices (ESD)
Single field that identifies component items that may be damaged by electrostatic/electromagnetic energy
Sensitive items are coded “Y”
ESD information is overlaid to API
API Subsystem

## Slide 218: Module 4 – API Subsystem
218
Program Select Override Data
Program Select Override data are displayed for information and cannot be entered on the IND screen
API Subsystem

## Slide 219: Module 4 – API Subsystem
219
Program Select Data
Program Select data can be entered when an indenture is established (Program Select Code and Program Begin Date are required)
Program Select data establishes Program Select Record which provides link between indenture and program
Program Select data may be added when fields are open (data can also be entered on Program Select (PS) screen)
API Subsystem

## Slide 220: Module 4 – API Subsystem
220
Enter Component Data
Step 11) Press enter to add component data and then press Done
API Subsystem

## Slide 221: Module 4 – API Subsystem
221
End of Lesson 4f
API Subsystem

## Slide 222
222
Course Evaluation

## Slide 223
448th Supply Chain Management Wing
The Supply Chain Delivers …
Parts on the Shelf and Contracts in Place